## Slide 1: Ministry of higher education and scientific research Middle Technical University Baquba Technical Institute Pathological analysis Department Medical Laboratory Instrument
Assist.prof. : Eman Ismail Momammed

## Slide 2
Lecture (10 ):
Microtome
It is an instrument which is used for cutting of materials in different thickness that are used as microscope slides , allowing samples to be observed under transmitted light or electron radiation
Microtomy is a method for the preparation of thin sections of materials such as bones, minerals and teeth for thorough examination. Microtome sections can be made thin enough with section thickness between 50 nm and 100 µm.

## Slide 3
Types of Microtome :
There are several types of microtome each designed for a specific purpose although many have a functional role , there are basic types of microtome are named according to the machine as following :
1-Rotary microtome : It is an excellent machine for research and is valuable from the preparation of serial section .

## Slide 4
2-Freezing microtome :It is using for cutting section when :
1-Speed of the utmost in portances .
2- When it is required to demonstrate fat histological .
3- When neurological structure are to be studies .
3-Ultra microtome :
4-Laser microtome .
5- Saw microtome :It is used for hard material such as teeth or bones.
6-Vibrating microtome : It used for difficult biological samples .
7- Sledge microtome .
8- cryo microtome .

## Slide 5
Parts of microtome :
1- Body with cover .
2- Operating handle with brake .
3- Knife .
4- Angle of tilt adjustment .
5- Base with knife carrier .
6- Knife clamps with screw .
7- Micron adjustment with thickness gauge .
8- Coarse adjustment of micron .

## Slide 6
Types of knives according to material that made of :
1 - Steel blades : There are used to prepare sections of animal or plant tissues for light microscopy histology.
2- Glass knives : are used to slice sections for light microscopy and to slice very thin sections for electron microscopy.
3- Diamond knives : are used to slice hard materials such as bone, teeth and plant matter for both light microscopy and for electron microscopy.
4- Gem quality diamond knives : are used for slicing thin sections for electron microscopy.

## Slide 7
Uses of microtomes :
1-Fix the paraffin block on block holder.
2- Rotate the operating handle and close the knife .
3- The section cutting effected by the vertical and fall of the object and fix the knife edge .

## Slide 8
Maintenance of microtomes:
1-Keep it clean from paraffin .
2- The sharpening of the knife is the main maintenance of microtomes

## Slide 9
Microtome

## Slide 10
Microtome