## Slide 1: Ministry of higher education and scientific research Middle Technical University Baquba Technical Institute Pathological analysis Department Medical Laboratory Instrument
Assist.prof. : Eman Ismail Momammed

## Slide 2
Lecture ( 4 ):
Lecture ( 4 )
Balance
Is essential laboratory instruments that are widely used for determining weight of various substances (powders ,crystals and chemical materials) in the laboratory for used to prepare reagents, stains and culture media , balances are required to weight accurately within the needed range.

## Slide 3
The balance should be kept clean and located in an area away from :
- large pieces of electrical equipment .
-open windows to minimize any vibration as interference that may happen.
** a slab of marble is placed under the balance.

## Slide 4
Types of balance :
1-Beam Balance: This type of balance uses a comparison technique in the form of a beam from which a weighing pan and scale pan are suspended. The object to be weighed is placed on the measuring pan, and standard weights are added to the scale pan until the beam is in equilibrium.

## Slide 5
2-Analytical Balance: It is used to measure mass to a very high degree of precision. The weighing pans are inside see-through enclosure with doors so that dust does not collect and so any air currents in the room do not affect the delicate balance
These balances are used:
1. To weigh small quantities usually in miligram(mg)
range.
2. When great accuracy is required .

## Slide 6
analytical balance

## Slide 7
Parts of analytical balance:
- Pan : Flat rigid support on which the specimen is placed .
- Glass doors : Sliding door that provide easy access to the
inside of the glass case.
- Digital readout : To show various numeric information .
- Zero button.
                - Calibration button .

## Slide 8
A- Single-Pan Mechanical Balance: These consist of :
- a beam with two knife-edges, one to support the weighing pan and the other acting as a pivot.
- fixed counterweight balances the load on the pan.
B-Two-Pan Analytical Balance: These balances consist of a symmetrical beam and three knife-edges. The two terminal knives support the pans and a central knife-edge acts as a pivot about which the beam swings
Types of Analytical Balance:

## Slide 9
C- Electronic Single-Pan Balance: These are top loading balances with the applied load being measured by an electromagnetic force unit or a strain gauged load cell. The mass of the load is proportional to the current needed to balance it. Single-pan electronic balances give a direct reading of the mass applied .

## Slide 10
D- Microbalance: This type of analytical balance is capable of measuring samples to at least (1) million parts of a gram. The more sensitive quartz crystal microbalance (QCM) measures mass by measuring the change in frequency of a piezoelectric quartz crystal

## Slide 11
Microbalance

## Slide 12
Use and care of balances:
1- Read carefully the manufacturer’s instructions
2- Always handle a balance with care.
3-Before starting to weigh, zero the balance as
directed by the manufacturer. If using a beam
balance, check the position of the beam.
4- Weight the chemicals at room temperature in a
weighing scoop or small beaker. Never put
the chemicals directly on the balance pan.
5-When adding or removing a chemical,
remove the container to avoid spilling any
chemical on the balance.

## Slide 13
6- Use small brush to remove any chemical
which may have been spilt on the balance.
7-Silica gel should be kept inside the analytical
balance case to remove any moisture present in
the atmosphere.
8-Keep the balance clean, being careful not to let
dirt accumulate near the pivots and bearings.
Use and care of balances: