## Slide 1: Ministry of higher education and scientific research Middle Technical University Baquba Technical Institute Pathological analysis Department Medical Laboratory Instrument
Assist.prof. : Eman Ismail Momammed

## Slide 2
Lecture ( 7 ) :
Flame photometer
It a device used for the determination of electrolytes in a given solution. It is most commonly used for the quantitative analysis of sodium ( Na ) and potassium ( K ) ions in body fluids. It used for measuring the wavelength specific for ( K , Na ) by special filter depending on intensity and emission light

## Slide 3
Parts of a flame photometer :
1-Source of flame :A burner that provides flame and can be maintained in a constant form and at a constant temperature.
2-Nebuliser and mixing chamber : Helps to transport the homogeneous solution of the substance into the flame at a steady rate and it has three inputs with atomizer which connect to the air gas and sample pressured air spry the sample and mixed with the gas in the chamber and blow to the burner and fuel inlet of gas and air inlet and sample capillary

## Slide 4
3-Optical system (optical filter):The optical system comprises three parts: convex mirror, lens and filter. The convex mirror helps to transmit light emitted from the atoms and focus the emissions to the lens. The convex lens help to focus the light on a point called slit. The reflections from the mirror pass through the slit and reach the filters. This will isolate the wavelength to be measured from that of any other extraneous emissions. Hence it acts as interference type color filters.

## Slide 5
4. Photo detector: Detect the emitted light and measure the intensity of radiation emitted by the flame.The emitted radiation is converted to an electrical signal with the help of photo detector. The produced electrical signals are directly proportional to the intensity of light.

## Slide 6
There are two types of atomizers burner:
1- Total consumption burner: It is draws the solution directly into the base of small flame where it is vaporized burned and locally droplets of fluid to the flame .
2- A premix burner: The large droplets full the floor of the chamber and only the rare fine droplets are carried up word into the flame by the flow of gas.

## Slide 7
component of a flame photometer

## Slide 8
Flame Colour | Emission wavelength ( nm ) | Element
Yellow | 589 | Sodium ( Na)
Violet | 766 | Potassium ( K)
Lime Green | 554 | Barium (Ba )
Orange | 622 | Calcium ( Ca )
Red | 670 | Lithium ( Li )
Flame photometer emission wavelength: