## Slide 1: Ministry of higher education and scientific research Middle Technical University Baquba Technical Institute Pathological analysis Department Medical Laboratory Instrument
Assist.prof. : Eman Ismail Momammed

## Slide 2
Lecture ( 9) :
pH Meter
It is a scientific instrument that measures the hydrogen-ion concentration in a solution indicating its acidity or alkalinity expressed as pH . pH is the unit that describes the degree of acidity or alkalinity. It is measured on a scale of 0 to 14.

## Slide 3
The pH value of a substance is directly related to the ratio of the hydrogen ion [H+] and the hydroxyl ion [OH-] concentrations.
*If the H+ concentration is greater than OH-, the material is acidic ( pH value is less than 7) .
*if the OH- concentration is greater than H+, the material is basic( pH value greater than 7) .
*if equal amounts of H+ and OH- ions are present, the material is neutral( pH of 7 ).

## Slide 4
Acids and bases have free hydrogen and hydroxyl ions, respectively. The term pH is derived from ( p ) the mathematical symbol for negative logarithm and ( H ) the chemical symbol for Hydrogen
The pH Scale

## Slide 5
pH indicators

## Slide 6
Parts of pH meters :
Electrode : There are two types of electrode :
A-Glass electrode ( Measuring electrode ) .
B-Reference electrode ( Calomel electrode ) .
Electrode holder .
Amplifier : It amplify the electrical charge which comes from electrode and pass to galvanometer as readable current .
Galvanometer or Digital display .
Temperature knob : To control the temperature and compensate the PH reading of solution .
Adjustment knob : To adjust the PH meter before taking the reading.

## Slide 7
pH meter measures the difference in electrical potential between a pH electrode and a reference electrode . The difference in electrical potential relates to the acidity or pH of the solution.
Types of pH meters:
Manual pH meter.
Digital pH meter

## Slide 8
Applications of pH meter :
know the acidity of the water .
Chemical laboratory analyses.
Soil measurements in agriculture .
Water quality for municipal water supplies .
Environmental remediation .
Brewing of wine or beer .
Healthcare and clinical applications such as blood chemistry.

## Slide 9
Maintenance of pH meters :
1-Rinse the electrode in distilled water after each
measurement .
2-Keep the electrode in distilled water after end of
experiment .
3-Electrode should not normally allowed to become dry .

## Slide 10
 | Lower Range | Upper Range
Tears | 6.5 | 7.6
Urine | 4.5 | 8.0
Saliva | 6.2 | 7.4
Blood | 7.2 | 7.45: Arterial: 7.4 ; Venous: 7.35
Gastric Secretion (in stomach lumen) | 1.0 | 2.0
Sputum | 7.54 (Normal) | 7.06 (uncontrolled asthma)
pH ranges for a healthy individual :