## Slide 1
Antiglobulin Cross-Match
Purpose
To detect incompatibility between donor and patient at 37C .
Scope & Application
This procedure applies to compatibility testing of all Multi-transfused patients and transfusion recipients who currently demonstrative or have a history of clinically significant antibodies .
Responsibility
It is the responsibility of the Medical Technologist ( Lab ) in the cross match facility of the red cell serology laboratory to perform the anti-globulin cross match using quality controlled reagents and proper dell concentrations . One MT performs the tests and another checks it . If any unexpected blood group antibody is detected , inform the staff of Advanced Red Cell Serology to carry out further investigations .

## Slide 2
Principle of cross match
The cross match through the anti globulin phase permits detection of clinical significant incompatibilities caused by incomplete antibodies that sensitized cells at 37C , but do not directly cause agglutination .

## Slide 3
( Procedure of cross match )
Label tube with patient / unit and test identification .
Add two drops of patient serum to each tube.
Prepare a 5% cell suspension in saline from each donor unit segment .
Add 1 drop of donor’s 5 % red cell suspension to the tube .
5. Incubate tubes at 37C for minimum 15 minutes . ( Follow manufacturer’s directions when using commercial reagents) .
6. Wash the cells a minimum of 3 times with saline . Decant completely after last wash ( washing can be done manually or in automated cell washer ) .
7. Add two drops of antihuman globulin reagent to the dry cell button .
8. Mix well and centrifuge at 1000 rpm for 1 minute .
9. Re-suspend and read for agglutination . Grade and record test results immediately.
10. To all negative anti-globulin tests add 1 drop of lgG-sensitized control cells . Centrifuge , resuspend and read for agglutination . Grade and record test results. After the addition of lgG - sensitised control cells to a negative test , the presence of agglutination indicates that the AHG serum added was capable of reacting and that the negative anti-globulin test is valid .

## Slide 4
Interpretation
Hemolysis or agglutination indicates the presence of a serologically incompatible cross -match . This result is interpreted as incompatible .
Absence of agglutination and hemolysis is a negative test result and indicates a serologically compatible cross-match. This result is interpreted as Compatible .
Documentation
Enter all results on the transfusion record card and OT/Ward transfusion register . Enter only the results of compatible units in the blood compatibility form . The Medical Technologist (Lab) who performed the test and the one who checked the results sign all records.