## Slide 1
Histology and anatomy
Theoretical
المعهد التقني بعقوبة
القسم :تقنيات التحليلات المرضية
المرحلة :الثانية
مدرس المادة:
م . م زويدة كاظم خضير الخالدي
ماجستير أحياء مجهرية

## Slide 3
Lec -1-
Microscope
microscope: is an instrument which is used for examination of fine structure of objects . Micro = small . Scope = to view. It enlarges of the images of the objects which then can be seen by the eye.

## Slide 4
Specifications of bright Field Microscope ( The Compound Microscope )
Commonly used in bacteriology laboratory.
It depends on light.
It consider as compound microscope.

## Slide 5
Types of Microscope:
1-Simple microscope :It is made of single or combination of lenses which act as single position convex lens .
2-Compound microscope : It is made up of 2 lenses which are fitted in a brass tube , one of the tubes can be slided into the other so that the distance between lenses can be changed and adjusted.
Other types of microscopes :
Bright field. is the simplest of all the optical microscopy illumination techniques. and the most common used microscope in the laboratories.
Dark-field. Dark-field microscope is used to observe live spirochetes.

## Slide 6
Phase – contrast. is used in biology to view unstained specimens. It is one of the types of microscopes used to study cells and cell parts like mitochondria, lysosomes and Golgi bodies. .
Fluorescent. Fluorescence microscope uses high-energy, short-wavelenght light that excites the electrons of certain molecules present within the sample.
Scanning electron. Scanning Electron Microscope is characterized as a microscope that has lower magnifying power but can provide 3 dimensional viewing of objects.

## Slide 7
Bright Field Microscope parts :
Base: The bottom support of the microscope.
Arm: It helps in holding the microscope.
Light source (illuminator): A light source mounted under the stage
Body tube: It hold the projector lenses that direct the light toward the ocular lenses.

## Slide 8
Nosepiece: Hold the objectives ( movable disk).
Coarse adjustment knob: Used to make relatively wide focusing adjustments to the microscope.
Fine adjustment Knob: Used to make relatively small adjustments to the microscope.
Stage: The flat plate where the slides are placed for observation.
Stage Clips: Clips on the stage used to hold the slide in place.
Condenser: Focuses the light through the specimen.
Iris diaphragm: Vary the amount of light passing through the stage opening.
Condenser adjustment knob: Used to move the condenser up and down.
Objective lenses: Primary magnification ( 4 ×, 10 ×, 40 ×, 100 ×).
Ocular lenses: Final magnification10 × (Eye Pieces).

## Slide 9
Steps for using of oil immersion lens :
Focus very carefully with the 40 x objective over the stained specimen on the slide.
Rotate the nose piece half way.
Apply a small drop of oil on the slide directly over the area of the specimen to be examined.
Rotate 100 x objective into the immersion oil.
Use the fine adjustment for focusing.

## Slide 10
Three important rules attend the use of oil immersion lens:
Never use an oil immersion lens without the oil.
Never get oil on any other lens.
Clean up all oil when finished.